AUTOSAR STARTUP SEQUENCE

STARTUP State
This state is divided into two parts, one before the OS is initialized and the other one post OS initialization. The main purpose of STARTUP state is to initialize the basic software modules.

RUN State
After all modules of basic software including OS and RTE have been initialized, The fixed EcuM module enters into RUN state.by the ECU State Manager Fixed module. It indicates the SW-Cs in the Application layer that the RTE and BSW are initialized and now it can start functioning.

SHUTDOWN State
It handles the controlled shutdown of basic software modules and results in one of the three selected shutdown targets for the ECU viz., SLEEP, OFF, or Reset. An important activity in this state is to write non-volatile data back to NVRAM.
SLEEP State
This is a power saving state in which no code is executed however there is still a constant supply of power to keep the ECU running. The SLEEP state provides a set of sleep modes referred to as shutdown targets. They provide a tradeoff between power consumption and time to restart the ECU.

WAKEUP State
The WAKEUP State is entered when the ECU comes out of the SLEEP state, due to wake up. It also provides a protocol to verify whether a wakeup event is valid and intended wakeup event or it was caused due to some erratic conditions. Let say A CAN bus communication link has been set up in the ECU. Whenever it receives a message it acts as a wakeup source for the ECU. However, it may be possible that due to some interference there may arise a voltage difference between CAN lines leading to CAN bus error. This is one of the erratic conditions which must be ignored by the ECU.